## Slide 1: Wood recruitment modeling in NetMap (or how to see the wood for the trees)
Sam Litschert & Lee Benda
Earth Systems Institute
Mount Shasta / Seattle / Fort Collins

## Slide 2
NetMap Analysis Tools developed with collaborators
Vegetation
-forest age
-fire risk
-burn severity
Query/Overlap tools & others
-menu driven: search & prioritize
e.g., high erosion w/best habitat,
high road density + high
erosion + sensitive habitat
Aquatic habitat indices
-intrinsic potential (species)
-core areas
-connectivity
-diversity
-floodplains
-bio-hotspots
-classification
EPA
Watershed Processes
-erosion/sediment supply
-LWD supply
-thermal loading/temp
USFS
Wild Salmon Center
Roads
-density (multi-scale)
-X w/fish
-upstream hab. length/quality
-stability
-drainage diversion
-surface erosion
NOAA

## Slide 3: Wood in streams
Legacy of management that reduced supplies of large woody debris
Functional importance of wood:
  create aquatic habitat,
  provide nutrients,
  channel morphology and sedimentation,
Processes that can provide wood are wildfire, insect, disease, wind, mass wasting, and suppression mortality
And now, thinning and tipping.
Harmon et al, 1986; FEMAT, 1993; Meleason et al, 2003

## Slide 4: Multi-scale wood modeling in NetMap
Reach scale
  Per 100m reach or project
  For selected piece sizes
  Temporally and spatially explicit
  Up to 3 stands on each bank
  Plots of volume and number of pieces
Watershed scale
  Temporally and spatially explicit
  CE analysis of management scenarios
  Based on RSWM technology
  Plots and maps available

## Slide 5
Reach Scale Wood Model (RSWM)
Stream reach
Forest stands
Forest stands
Hillslope gradients
Channel
width
Stand
widths
Mortality types include suppression, fire, insect, disease, & wind-throw.
Bells and Whistles:
channel width,
stand width,
hillslope gradient,
bank erosion,
wood decay,
taper equations,
thinned trees that are tipped, and
size of resulting wood pieces
Inputs: stand tables from forest growth models
Outputs: 10 types of plots
Kozak, 1988; Bilby et al, 1999; Benda and Sias 2003; Sobota et al, 2006; Hibbs et al, 2007; and more.

## Slide 6
RSWM Scenarios
Left bank is always no action scenario (70 m)
Right bank treatment scenarios (11)
Double entry thin, 70 TPA: 2010, 2040
All other parameters held constant
Right bank scenarios | 
Stand1 | Stand2
No action (10 m) | No action (60 m)
No action | Thinned
No action | Thin & tip 5%
No action | Thin & tip 10%
No action | Thin & tip 15%
No action | Thin & tip 20%
Thinned (70 m) | 
Thin & tip 5% | 
Thin & tip 10% | 
Thin & tip 15% | 
Thin & tip 20% | 

## Slide 7
Chart: Cumulative wood volume using 2 bank scenarios, no buffer
Untreated / Untreated | 0.0087996 | 0.25385 | 1.2976 | 2.4553 | 3.7623 | 5.1694 | 6.6713 | 8.2403 | 9.8043 | 11.3769 | 12.9061 | 14.4612 | 16.0393 | 17.5484 | 19.0038 | 20.51 | 21.832 | 23.2338 | 24.5722 | 25.6344 | 26.6173
Untreated/Double thin | 0.0065454 | 0.16186 | 0.80563 | 1.5201 | 2.3204 | 3.1991 | 4.1405 | 4.9285 | 5.7632 | 6.6075 | 7.4361 | 8.2816 | 9.1361 | 9.9754 | 10.795 | 11.6476 | 12.4148 | 13.2328 | 14.0275 | 14.6915 | 15.3239
Untreated/Double thin, tip 5 | 4.7267 | 4.4976 | 4.7907 | 5.185 | 5.6927 | 6.3037 | 9.9559 | 10.2744 | 10.6803 | 11.1326 | 11.6026 | 12.1197 | 12.6733 | 13.2366 | 13.8029 | 14.4229 | 14.9764 | 15.5979 | 16.2118 | 16.7094 | 17.1885
Untreated/Double thin, tip 10 | 7.9541 | 7.4608 | 7.513 | 7.6875 | 7.9945 | 8.422 | 14.0822 | 14.0567 | 14.1496 | 14.3172 | 14.5276 | 14.808 | 15.1456 | 15.5113 | 15.897 | 16.3516 | 16.7537 | 17.2362 | 17.7227 | 18.1033 | 18.4749
Untreated/Double thin, tip 15 | 10.1023 | 9.4328 | 9.3245 | 9.3525 | 9.5258 | 9.8311 | 17.3512 | 17.0556 | 16.9028 | 16.8463 | 16.8523 | 16.9461 | 17.113 | 17.3227 | 17.5655 | 17.8892 | 18.1712 | 18.5436 | 18.9289 | 19.2165 | 19.5027
Chart: Cumulative wood volume using 2 bank scenarios, 10 m buffer
Untreated / Untreated | 0.0087996 | 0.25385 | 1.2976 | 2.4553 | 3.7623 | 5.1694 | 6.6713 | 8.2403 | 9.8043 | 11.3769 | 12.9061 | 14.4612 | 16.0393 | 17.5484 | 19.0038 | 20.51 | 21.832 | 23.2338 | 24.5722 | 25.6344 | 26.6173
Untreated/Buffer10_Double thin | 0.0087996 | 0.24915 | 1.2687 | 2.3915 | 3.6402 | 4.9778 | 6.3922 | 7.7936 | 9.1831 | 10.5578 | 11.8765 | 13.1927 | 14.4999 | 15.7457 | 16.933 | 18.1436 | 19.1979 | 20.3024 | 21.3453 | 22.1719 | 22.9292
Untreated/Buffer10_Double thin tip 10% | 2.0335 | 2.1127 | 2.9847 | 3.9725 | 5.0973 | 6.3214 | 10.2818 | 11.3662 | 12.4664 | 13.577 | 14.6544 | 15.7499 | 16.8552 | 17.9158 | 18.9334 | 19.9884 | 20.8998 | 21.873 | 22.7952 | 23.5108 | 24.1659
Untreated/Buffer10_Double thin tip 15% | 2.2595 | 2.3212 | 3.1772 | 4.1502 | 5.2616 | 6.4731 | 11.3959 | 12.3901 | 13.4079 | 14.4433 | 15.4519 | 16.4844 | 17.532 | 18.5397 | 19.5088 | 20.5192 | 21.3896 | 22.3252 | 23.2128 | 23.8965 | 24.5223
Untreated/Buffer10_Double thin tip 20% | 2.2799 | 2.3402 | 3.1948 | 4.1665 | 5.2767 | 6.4871 | 12.1374 | 13.0722 | 14.0358 | 15.0215 | 15.9846 | 16.9754 | 17.9847 | 18.9574 | 19.8942 | 20.8749 | 21.7181 | 22.6286 | 23.4931 | 24.1555 | 24.7618
The buffer reduces the effect of the thin and tip by reducing loss of wood. But in the long term the volume of wood in the stream increased to close to the untreated scenario.
Scenarios with tipped trees produce higher volumes of wood in the reach than untreated or thinned stands for most of the time simulated.

## Slide 8
Chart: Wood volume by distance to stream using 2 bank scenarios, no buffer
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
Untreated / Untreated | 0.0087996 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Untreated/Double thin | 0.0087996 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Untreated/Double thin, tip 5 | 1.5805 | 1.5328 | 1.0984 | 0.42861 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Untreated/Double thin, tip 10 | 1.5805 | 1.5328 | 1.0984 | 0.99918 | 0.84012 | 0.77185 | 0.69151 | 0.10585 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Untreated/Double thin, tip 15 | 1.5805 | 1.5328 | 1.0984 | 0.99918 | 0.84012 | 0.77185 | 0.69151 | 0.62869 | 0.47466 | 0.41644 | 0.35449 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Wood volume by distance to stream using 2 bank scenarios, with buffer
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
Untreated / Untreated | 0.0087996 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Untreated/Buffer10_Double thin | 0.0087996 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Untreated/Buffer10_Double thin tip 10% | 0.0087996 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.35449 | 0.29639 | 0.14023 | 0.056577 | 0.049536 | 0.043287 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Untreated/Buffer10_Double thin tip 10% | 0.0087996 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.35449 | 0.29639 | 0.14023 | 0.056577 | 0.049536 | 0.043287 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Untreated/Buffer10_Double thin tip 15% | 0.0087996 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.35449 | 0.29639 | 0.14023 | 0.056577 | 0.049536 | 0.043287 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Year = 2010
1st thin
RSWM was run to 70m on both banks, trees are too small to contribute beyond 26m from reach
Untreated stands contributed no wood in 2010

## Slide 9: Total volume of cumulative wood over time (sorted by increasing volume)
Total cumulative wood | Volume (m3 100 m-1 reach) (percent change from reference )
Untreated/Double thin | 156 (-42%)
Untreated/Double thin, tip 5% | 232 (-14%)
Untreated/Buffer10_Double thin | 243 (-10%)
Untreated/Untreated (reference condition) | 271
Untreated/Double thin, tip 10% | 284 (5%)
Untreated/Buffer10_Double thin tip 10% | 288 (6%)
Untreated/Buffer10_Double thin tip 15% | 299(10%)
Untreated/Buffer10_Double thin tip 20% | 305 (13%)
Untreated/Double thin, tip 15% | 324 (20%)
Tree tipping from thinning operations combined with riparian buffers offer the highest volumes of wood loadings

## Slide 10
Watershed Scale Wood Model
Stand tables from forest growth models (FVS, Organon and Zelig) pre-processed in RSWM
Tabular data integrated with GIS: stream reaches, stands, and DEM
Generate output:
plots and maps

## Slide 11: Stand information
Watershed area = 5 km2
Coho and steelhead habitat
Km

## Slide 12: Stand treatments – thin to 70 TPA from the bottom (47% of watershed thinned)

## Slide 13: Stand treatments – no action buffer & thin (39% of watershed thinned)

## Slide 14: Wood volume (or number of pieces) sources for no action, year = 2065
Stand tables not available for all locations, no wood recruited, or pieces too small
Low
High
Volume per length per year

## Slide 15: Comparison of wood volume for no action and thinned buffers
Wood
volume

## Slide 16: Wood volume by time (m3 100m-1 yr-1) Thinned 2015
No action buffer
Thinned buffer
1995: high initial mortality – FVS model parameters?
2015: thinned
2025 – 2085: no action buffer produces more wood
2095+ : thinned buffer scenario produces more wood
Only one stand had data to 2295, others ended at 2195, hence the low values after 2195

## Slide 17: Wood volume by piece size and time (m3 100m-1 yr-1), thinned 2015
No action buffer
Thinned buffer
Thinned buffers resulted in a 15% decrease in wood volume

## Slide 18: Percent changes in wood volume by piece size (cm) from no action to thinned buffer
Decrease in wood of smaller sizes
Increase in wood of larger sizes
Chart: 
| 0 | 10 | 35 | 60 | 80 | Total
% change from No thin buffer | -4.489 | -33.5187 | -16.5553 | 31.5199 | 13.4552 | -15.4878

## Slide 19: Applications for land management
  Multi-scale: reach or project scale v. watershed scale management and analysis;
  Enables spatially variable approach and analysis;
  Designs for riparian treatments – thinning, buffers, habitat;
  Designs for mitigation,
  enhancement, tree tipping

## Slide 20: Acknowledgements and thanks to: USFS-PNW, Gordon Reeves, Stu Johnston, Jack Sleeper, and Dan Miller netmaptools.org earthsystems.net

## Slide 21: Large woody debris
Chart: Cumulative volume of wood recruited after two thin and tip treatments (2015, 2045)
| 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050 | 2055 | 2060 | 2065
No treatment 240' | 0.0043998 | 0.12693 | 0.64878 | 1.2276 | 1.8812 | 2.5847 | 3.3357 | 4.1201 | 4.9021 | 5.6884 | 6.453
TreeHt240_thin | 0.0043998 | 0.12652 | 0.64637 | 1.2212 | 1.8625 | 2.5515 | 3.2815 | 4.011 | 4.7328 | 5.4435 | 6.1189
TreeHt240_thin_tip5% | 0.23612 | 0.33919 | 0.84168 | 1.4006 | 2.0275 | 2.7033 | 4.3985 | 5.0337 | 5.6697 | 6.3027 | 6.9071
TreeHt240_thin_tip10% | 0.24445 | 0.34688 | 0.84878 | 1.4072 | 2.0336 | 2.7089 | 5.0311 | 5.6145 | 6.2035 | 6.7934 | 7.3586
Chart: Wood volume by distance to reach: 40m stand (yr. = 2045)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36
No treatment | 0.03628 | 0.028242 | 0.019173 | 0.017088 | 0.015381 | 0.013875 | 0.01246 | 0.010933 | 0.0098122 | 0.0087766 | 0.0078184 | 0.0061988 | 0.0054636 | 0.0048151 | 0.0034998 | 0.0030574 | 0.0026237 | 0.0022487 | 0.0013561 | 0.001175 | 0.0010121 | 0.00084772 | 0.00038571 | 0.00032781 | 0.00027158 | 8.587e-05 | 6.9572e-05 | 5.4022e-05 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
TreeHt120_thin | 0.03628 | 0.028242 | 0.019173 | 0.017088 | 0.015381 | 0.013875 | 0.01246 | 0.010933 | 0.0098122 | 0.0087766 | 0.0078184 | 0.0061988 | 0.0054636 | 0.0048151 | 0.0034998 | 0.0002303 | 0.0002094 | 0.00018936 | 0.00017026 | 0.00015216 | 0.00013512 | 0.00011918 | 0.0001044 | 9.0807e-05 | 7.8424e-05 | 6.728e-05 | 5.6881e-05 | 4.6486e-05 | 3.7545e-05 | 1.6399e-05 | 1.306e-05 | 1.0072e-05 | 3.0454e-06 | 2.3204e-06 | 5.1265e-07 | 3.8356e-07
TreeHt120_thin_tip5% | 0.03628 | 0.028242 | 0.019173 | 0.017088 | 0.015381 | 0.013875 | 0.01246 | 0.010933 | 0.0098122 | 0.0087766 | 0.0078184 | 0.0061988 | 0.0054636 | 0.0048151 | 0.0034998 | 0.2764 | 0.19204 | 0.00018936 | 0.00017026 | 0.00015216 | 0.00013512 | 0.00011918 | 0.0001044 | 9.0807e-05 | 7.8424e-05 | 6.728e-05 | 5.6881e-05 | 4.6486e-05 | 3.7545e-05 | 1.6399e-05 | 1.306e-05 | 1.0072e-05 | 3.0454e-06 | 2.3204e-06 | 5.1265e-07 | 3.8356e-07
TreeHt120_thin_tip10% | 0.03628 | 0.028242 | 0.019173 | 0.017088 | 0.015381 | 0.013875 | 0.01246 | 0.010933 | 0.0098122 | 0.0087766 | 0.0078184 | 0.0061988 | 0.0054636 | 0.0048151 | 0.0034998 | 0.2764 | 0.25565 | 0.17816 | 0.00017026 | 0.00015216 | 0.00013512 | 0.00011918 | 0.0001044 | 9.0807e-05 | 7.8424e-05 | 6.728e-05 | 5.6881e-05 | 4.6486e-05 | 3.7545e-05 | 1.6399e-05 | 1.306e-05 | 1.0072e-05 | 3.0454e-06 | 2.3204e-06 | 5.1265e-07 | 3.8356e-07

## Slide 23: Wood number of pieces Year = 2065
Low
High

## Slide 24: What is NetMap and Why would I want to use it?
Comprised of integrated tools and geospatial data
Standardized GIS data is ready to analyze
Applies science-based models
Built on existing technologies
Developed through collaborative relationships
Increasing area for planning means more time spent on analysis
Overlapping agency jurisdictions
Similar questions, data and analysis needs
(Life without NetMap ;-)

## Slide 25
NetMap data
Universal digital landscapes
DEM-derived streams
~100 stream attributes
Completed
Pending
S.E. Alaska and
British Columbia
Western US
Integrated NetMap Components
NetMap tools
Channel geomorphology
Riparian management
Aquatic habitat
Basin hydrology
Erosion
Roads
Vegetation
NetMap coverage
Help
Indexed and searchable
Online videos
Webinars available
One-on-one

## Slide 26: Legal challenges to CEs analyses
CEs analyses did not account for disturbances over time;
Models were not sufficiently evaluated with measured data; and
Model assumptions were inadequately disclosed.
From reviews by Smith, 2005; Reid, 2006

## Slide 27: Cumulative Watershed Effects (CEs)
The physical and ecological effects that result from multiple land use disturbances over space and time;
Land managers may be required to:
  Compare the CEs of different forest management scenarios, and
  Account for “past, present, and reasonably foreseeable future” impacts;
Which management scenario results in more CEs?
Watershed
Streams
Treatment polygons
CEQ, 1997